Summary

To facilitate the evaluation of inverters, charge controllers, PCUs and other power handling devices a test-rig was built with two AC and two DC meters. This document lists the specifications and details of this test-rig.

Specification

The test-rig has the following limits and capabilities:

Metering

There are two DC meters and two AC meters, purchased from ElMeasure, the range of measurement for each is outlined below

DC meters

•    Model : ElMeasure EDC1100

•    Voltage : 0 – 150V

•    Current : 0 – 50A

•    Accuracy : Class I

•    Display : 1 line 6 figure LCD

•    Input: two push buttons to scroll through display, and for setup

•    Parameters measured: Voltage, Current, Power, Watt Hours

AC meters

•    Model : ElMeasure LG+5310

•    Voltage : 0 – 415V

•    Current : 0 – 20A

•    Accuracy : Class I

•    Display : 3 x 1 line 6 figure LCD

•    Input: two push buttons to scroll through display, and for setup

• 	Parameters measured: Voltage, Current, Frequency, Real Power, Reactive Power, Volt Amps, Power Factor, Watt Hours, Load Hours.

Connections

There are four lug terminals to connect the inputs and outputs. These are rated at 50A.

Power

The meters require an auxiliary power supply, provided via a three pin AC PC type socket. Burden is nominally around 4VA for each meter.

Communication

The diagram below shows the flow of information for the test-rig.

Meter box

RS485

RS232

RS232

USB

Raspberry Pi

SD

USB

PC

WiFi

Slave network

RS485                           RS232              USB

Conversion network

storage

Master network

Dropbox

WiFi

SSH

Drawing 1: System communication flow

•    Slave network: 4 meters communicating over RS485*

•    Conversion network: RS485 to USB

◦ RS485 to RS232* – Hexin 2108B, requiring a 9V DC supply

◦ RS232 to USB* – Prolific Technology PL2303, power from USB, requires installation of a driver

•    Master network: logging control and storage

◦ The Raspberry Pi (RPi) reads and logs data

◦ The setup of the log is done on a PC, communicating over SSH* with the RPi

◦ Storage is on the RPi and there is an option of uploading data to dropbox, for easier access and monitoring.

- For an explanation of the communication protocols used please refer to the appendix

Physical Design

DC 2

DC 1

AC 2

AC 1

DC 1 (Solar)

AC 1 (Grid)

RS485 communication

DC 2 (Battery)           AC 2 (Load)

Meter power supply

Drawing 2: Physical layout

DC2

out

Back

AC2

AC2

out

DC1in                    DC1out

Front

AC1in                     AC1out

Drawing 3: Top panel connection layout

Electrical connection

AC1

out

AC2

in             out

DC1 DC1

out

DC2

in             out

Aux -                  N Aux +

Aux - Aux +

DC Meter 1

EDC1100

RS485+ RS485-

RS485+ RS485-

50A – 75mA

shunt

AC Meter 1    R   S1

LG+5310             2

IN                            CH  -

IN                                     1 +

30:5 current transformer

Aux -                  N Aux +

Aux - Aux +

DC Meter 2

EDC1100

Earth casing

RS485+ RS485-

30:5 current transformer

RS485+ RS485-

50A – 75mA

shunt

AC Meter 2    R   S1

LG+5310             2

IN                            CH +

IN                                     1  -

Drawing 4: Electrical connection diagram for meter box

Operation

The test-rig can be used to measure any AC or DC devices within the limits listed above. For example, a connection diagram and sketch of the physical connections for testing a Solar-PCU are shown below. Please refer to the software guide for setting up the data logging and communication.

Grid

DC

DC

Solar            DC

DC

Solar + Grid       AC

PCU

AC

Load

DC

DC

Battery

Drawing 5: Connection diagram for Solar-PCU testing

Battery

To PCU Battery output

Back

From PCU Load output

Load

Front

To PCU PV input

Grid

To PCU Grid input

Drawing 6: Physical connection sketch for Solar-PCU testing

Appendix

Communication protocols and transmission specifications used

RS485

This refers to TIA-485-A transmission specification. In particular the ElMeasure meters use half- duplex transmission on a twisted pair. The advantage of RS485 over RS232 is that it uses a differential pair to communicate. As noise often affects the common mode of a signal a differential pair has a better noise rejection. Hence RS485 is suitable for use over long distances (around

1.2km), so is commonly used for industrial metering and control equipment.

RS232

A common specification. This is used as an intermediary between RS485 and USB, simply because an RS485 to USB converter could not be found

USB

A common specification.

Modbus RTU

The Modbus RTU protocol is us is used by the ElMeasure meters for communication. A Modbus guide is included with the communication which was found a help in understanding how to use modbus.

SSH

Secure SHell (SSH) is used to remotely log into the RPi and control the data logging/ download data.

# Text boxes

in

DC2

in

in

AC1

AC2

in

DC2

V

+

V

R

S

A

V

-

V

+

V

R

S

A

V

-

V

A

A

V

A

V

A

V

PV