; ****************************************************************
; Serial Port communications with PN532 RFID board.
;
; Assumes that we are using the default 8-MHz internal clock.
;
; All routines will exit pointing to bank0.
; ****************************************************************
;
        LIST P=PIC16F688
        #INCLUDE <p16f688.inc>

        ERRORLEVEL	0,	-302	;suppress bank selection messages

        __CONFIG _FOSC_INTOSCIO & _WDT_OFF & _PWRTE_ON & _MCLRE_OFF & _BOD_OFF & _CPD_OFF & _CP_OFF

; LCD interface defines
LCD_Data4 EQU 0 ;RC0: LCD data line 4
LCD_Data5 EQU 1 ;RC1: LCD data line 5
LCD_Data6 EQU 2 ;RC2: LCD data line 6
LCD_Data7 EQU 3 ;RC3: LCD data line 7
#define LCD_TRIS TRISC
#define LCD_PORT PORTC
#define Max_Line 8 ;Max hex chars per line (1 hex = 2 ASCII)

#define Trail_Blk 11 ;ID of Trailer Block (holds keys)
#define Data_Blk 10 ;ID of Data Block (holds credits)
#define Resp_TFI 0xD5 ;TFI for response messages from reader

#define Def_Key1 0xFF ;first byte of default key
#define Def_Key2 0xFF
#define Def_Key3 0xFF
#define Def_Key4 0xFF
#define Def_Key5 0xFF
#define Def_Key6 0xFF ;last byte of default key

; PORTA Defines
#define Enable_T TRISA, 0 ;LCD enable
#define Enable PORTA, 0 ;LCD enable
#define Select_T TRISA, 1 ;LCD cmd/data mode select
#define Select PORTA, 1 ;LCD cmd/data mode select

Cmnd_Mode EQU 00 ;LCD register select command mode
Data_Mode EQU 01 ;LCD register select data mode

;Defines
RX_Port EQU 05 ;PORTC5 - Serial receive
TX_Port EQU 04 ;PORTC4 - Serial transmit (unused)

Bank0_Data UDATA 0x20 ;Bank 0 data
Delay_Cnt RES 1 ;Delay Counter
LCD_Data RES 1 ;Temporary holder for LCD data
Reg_Select RES 1 ;LCD register select flag
BCD_Byte RES 1 ;used for conversion to ASCII
Dummy RES 1 ;dummy variable
Temp_ASC RES 1 ;Temporary variable used in Make_ASCII
Byte_Count RES 1 ;byte counter
RX_Byte RES 1 ;serial receive byte
New_Msg RES 1 ;new message received flag
Save_W RES 1 ;save the W register during interrupts
Save_Status RES 1 ;save the Status register during interrupts
Checksum RES 1 ;checksum for commands
UID1 RES 1 ;user ID of card/tag
UID2 RES 1 ;user ID of card/tag
UID3 RES 1 ;user ID of card/tag
UID4 RES 1 ;user ID of card/tag
Tag_Blk_Num RES 1 ;Tag Block Number
Read_Cnt RES 1 ;counter for reading receive buffer
Targ_Ptr RES 1 ;pointer to target value for buffer read
TFI_Found RES 1 ;TFI was found in the response message
Cmd_Echo RES 1 ;byte after TFI in response
Cmd_Stat RES 1 ;command status in response
Line_Brk RES 1 ;LCD line break after this value
Disp_All RES 1 ;1: display entire receive buffer
        ;0: display just data bytes
Junk_Num RES 1 ;junk number for write to tag

Tag_Message UDATA 0x50
Byte1 RES 1 ;First byte
Byte2 RES 1
Byte3 RES 1
Byte4 RES 1
More_Bytes RES d'15' ;only needed during debug to dump data

;-----------------------------------
; Program code starts here
;-----------------------------------

RESET CODE 0x00
        GOTO Init

;Interrupt Handler
Int_Vec CODE 0x04
        BCF PIE1, RCIE ;serial RX interrupt enable
        MOVWF Save_W
        SWAPF STATUS, W
        MOVWF Save_Status
Chk_Ovr BTFSS RCSTA, OERR ;receive buffer overflow error:
        GOTO RX_Int1 ;no
        CALL Overflow
        GOTO Ret_Prep

RX_Int1 MOVFW RCREG ;read RX buffer (clears interrupt)
        MOVWF RX_Byte
        BTFSC New_Msg, 0 ;first character of new message?
        GOTO RX_Int2 ;no
        CLRF Byte_Count

RX_Int2 BSF New_Msg, 0
        MOVLW LOW Byte1
        ADDWF Byte_Count, W
        MOVWF FSR
        MOVFW RX_Byte
        MOVWF INDF ;save to buffer as indexed by Byte_Count
        INCF Byte_Count, F

RX_Int3 MOVFW RX_Byte
        BTFSC PIR1, RCIF ;another RX interrupt?
        GOTO Chk_Ovr ;yes

Ret_Prep SWAPF Save_Status, W
        MOVWF STATUS
        SWAPF Save_W, F
        SWAPF Save_W, W
        BSF PIE1, RCIE ;serial RX interrupt enable
        RETFIE

;Main code
Init NOP ;error if go directly to BANKSEL
        BANKSEL TRISA ;bank1
        BCF Enable_T ;output
        BCF Select_T ;output
        BCF LCD_TRIS, LCD_Data4
        BCF LCD_TRIS, LCD_Data5
        BCF LCD_TRIS, LCD_Data6
        BCF LCD_TRIS, LCD_Data7
        CLRF ANSEL ;set all as digital
        MOVLW 0x70
        MOVWF OSCCON ;set for 8-MHz internal clock
        BSF PIE1, RCIE ;serial RX interrupt enable

        BANKSEL PORTA ;bank0
        MOVLW 0x07
        MOVWF CMCON0 ;turn off comparators
        CLRF Byte_Count
        CLRF New_Msg
        CLRF Disp_All
        CALL Init_Serial

        BTFSS STATUS, NOT_TO ;reset due to WDT?
        GOTO Scan_Loop ;yes
        CALL Delay100ms ;wait for LCD to get ready
        CALL Init_LCD
        CLRF Junk_Num

Module_Init CALL Send_Init
        BTFSS New_Msg, 0 ;response from reader?
        GOTO Module_Init ;no

Scan_Loop MOVLW Data_Blk
        MOVWF Tag_Blk_Num

        ;Find a tag
        CALL Scan_Tag
        CALL Disp_UID ;comment out if not needed

        ;Found a Tag so authorize for reads/writes
        CALL Auth_Tag
        CALL Auth_Msg ;comment out if not needed

        ;Write to tag
        CALL Write_Tag
        CALL Send_Data

        ;Read data
        CALL Read_Tag

        ;Change values to write (debug)
        MOVLW 0x11
        ADDWF Junk_Num, F

        ;Dump what was read (debug)
        CALL Find_Resp
        CALL Disp_Buff
        CALL Delay1sec
        CALL Delay1sec
        CALL Delay1sec

        CALL Done_Msg

        GOTO Scan_Loop

;-----------------------------------
; RFID Messages
;-----------------------------------

;Initialize and wakeup RFID module
Send_Init MOVLW 0x55
        CALL TX_Serial
        MOVLW 0x55
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial ;add more zeros if needed to wake up

        ;Need to send SAM Config to get out of Low Vbat state
        CALL Preamble
        MOVLW 0x03
        CALL TX_Serial
        MOVLW 0xFD
        CALL TX_Serial
        MOVLW 0xD4
        CALL TX_Serial
        MOVLW 0x14 ;SAMConfiguration
        CALL TX_Serial
        MOVLW 0x01
        CALL TX_Serial
        MOVLW 0x17
        CALL TX_Serial
        GOTO Postamble

Send_ACK MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0xFF
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0xFF
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        RETURN

;Get RFID module firmware version number (contained in
;the last three data words of the response message)
;Example: 01 06 07 is version 1.6.7
Firmware CALL Preamble
        MOVLW 0x02
        CALL TX_Serial
        MOVLW 0xFE
        CALL TX_Serial
        MOVLW 0xD4
        CALL TX_Serial
        MOVLW 0x02 ;GetFirmwareVersion
        CALL TX_Serial
        MOVLW 0x2A
        CALL TX_Serial
        GOTO Postamble

;Look for a tag
Scan_Tag CALL Preamble
        MOVLW 0x04
        CALL TX_Serial
        MOVLW 0xFC
        CALL TX_Serial
        MOVLW 0xD4
        CALL TX_Serial
        MOVLW 0x4A ;InListPassiveTarget
        CALL TX_Serial
        MOVLW 0x01 ;read one card (max=2)
        CALL TX_Serial
        MOVLW 0x00 ;106-kbps type A
        CALL TX_Serial
        MOVLW 0xE1
        CALL TX_Serial
        CALL Postamble
        CALL Scan_Msg
        CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Scan_Tag
        CALL Get_UID
        RETURN

;Last four data words in the scan response are UID
;for Mifare Classic tags
Get_UID MOVLW d'8' ;offset from TFI to UID
        ADDWF Targ_Ptr, F
        MOVLW LOW Byte1
        ADDWF Targ_Ptr, W ;index to RFCID
        MOVWF FSR
        MOVFW INDF
        MOVWF UID1
        INCF FSR, F
        MOVFW INDF
        MOVWF UID2
        INCF FSR, F
        MOVFW INDF
        MOVWF UID3
        INCF FSR, F
        MOVFW INDF
        MOVWF UID4
        RETURN

;Authorize tag data sector using the defined Trailer block ID
Auth_Tag CALL Preamble
        MOVLW 0x0F
        CALL TX_Serial
        MOVLW 0xF1
        CALL TX_Serial
        MOVLW 0xD4
        MOVWF Checksum
        CALL TX_Serial
        MOVLW 0x40 ;InDataExchange
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x01 ;number of targets
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x60 ;authenticate with Key A
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Trail_Blk ;Trailer block for data sector
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Def_Key1 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Def_Key2 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Def_Key3 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Def_Key4 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Def_Key5 ;yes
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW Def_Key6 ;yes
        ADDWF Checksum, F
        CALL TX_Serial ;end Key A
        MOVFW UID1 ;tag UID (4 bytes)
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW UID2
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW UID3
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW UID4
        ADDWF Checksum, F
        CALL TX_Serial ;end tag UID
        CALL Do_Chksm
        CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Bad_Scan
        MOVFW Cmd_Stat
        BTFSS STATUS, Z
        GOTO Bad_Scan
        RETURN

;Read tag data from the defined data block of the authorized sector
Read_Tag CALL Preamble
        MOVLW 0x05
        CALL TX_Serial
        MOVLW 0xFB
        CALL TX_Serial
        MOVLW 0xD4
        MOVWF Checksum
        CALL TX_Serial
        MOVLW 0x40 ;InDataExchange
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x01 ;number of targets
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x30 ;read block (16 bytes)
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Tag_Blk_Num ;block number (0-63)
        ADDWF Checksum, F
        CALL TX_Serial
        GOTO Do_Chksm

;Initiates a write to the tag.
Write_Tag CALL Preamble
        MOVLW 0x15
        CALL TX_Serial
        MOVLW 0xEB
        CALL TX_Serial
        MOVLW 0xD4
        MOVWF Checksum
        CALL TX_Serial
        MOVLW 0x40 ;InDataExchange
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0x01 ;number of targets
        ADDWF Checksum, F
        CALL TX_Serial
        MOVLW 0xA0 ;write block (16 bytes)
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Tag_Blk_Num ;block number (0-63)
        ADDWF Checksum, F
        CALL TX_Serial
        RETURN

;Sends 16 bytes of data as part of the Write_Tag command.
Send_Data MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        MOVFW Junk_Num
        ADDWF Checksum, F
        CALL TX_Serial
        COMF Junk_Num, W
        ADDWF Checksum, F
        CALL TX_Serial
        CALL Do_Chksm
        CALL Find_Resp
        BTFSS TFI_Found, 0
        GOTO Bad_Write
        MOVFW Cmd_Stat
        BTFSS STATUS, Z
        GOTO Bad_Write
        RETURN

Preamble CLRF New_Msg
        CLRF Byte_Count
        MOVLW LOW Byte1 ;clear receive buffer
preamble1 MOVWF FSR
        MOVLW 0x00
        MOVWF INDF
        INCF FSR, F
        INCF Byte_Count, F
        MOVLW d'31'
        SUBWF Byte_Count, W
        BTFSS STATUS, Z
        GOTO preamble1
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0x00
        CALL TX_Serial
        MOVLW 0xFF
        CALL TX_Serial
        RETURN

Do_Chksm COMF Checksum, F ;negate value (1's complement)
        INCF Checksum, W ;add 1 for 2's complement
        CALL TX_Serial
Postamble MOVLW 0x00
        CALL TX_Serial
        CALL Delay100ms
        RETURN

Find_Resp CLRF TFI_Found
        MOVFW Byte_Count
        SUBLW d'15'
        BTFSS STATUS, C ;more than just ACK?
        GOTO find_resp1 ;yes
        CLRF New_Msg
        RETURN
find_resp1 CALL Send_ACK
        MOVLW d'20'
        MOVWF Read_Cnt
        MOVLW Resp_TFI ;Response TFI
        CALL Read_Buff
        INCF Targ_Ptr, W
        BTFSS STATUS, Z ;target found?
        BSF TFI_Found, 0
        RETURN

;-----------------------------------
; Receive Buffer Utilities
;-----------------------------------

Read_Buff CLRF Targ_Ptr
read_buff1 MOVLW LOW Byte1
        ADDWF Targ_Ptr, W
        MOVWF FSR
        MOVFW INDF ;read from memory as indexed by Targ_Ptr
        SUBLW Resp_TFI ;Response TFI
        BTFSS STATUS, Z ;found target value?
        GOTO read_buff2 ;no

        INCF FSR, F
        MOVFW INDF ;command echo (=command+1)
        MOVWF Cmd_Echo
        INCF FSR, F
        MOVFW INDF ;command status
        MOVWF Cmd_Stat
        RETURN

read_buff2 INCF Targ_Ptr, F
        DECF Read_Cnt, F
        BTFSS STATUS, Z ;completed read?
        GOTO read_buff1 ;no
        MOVLW 0xFF
        MOVWF Targ_Ptr
        RETURN ;value not found

;Display receive buffer
Disp_Buff CLRF New_Msg
        CLRF Dummy
        MOVLW Max_Line
        MOVWF Line_Brk
        CALL Clear_LCD
        BTFSC Disp_All, 0 ;display entire buffer?
        GOTO disp_loop ;yes
        CALL Find_Resp ;no, just display data
        MOVFW Targ_Ptr
        BTFSC STATUS, Z ;found valid response?
        RETURN ;no
        ADDLW d'3' ;point to start of data
        MOVWF Dummy
        ADDWF Line_Brk, F
        MOVLW d'16'
        MOVWF Byte_Count

disp_loop MOVLW LOW Byte1
        ADDWF Dummy, W
        MOVWF FSR
        MOVFW INDF ;read from memory as indexed by Dummy
        CALL Make_ASCII
        INCF Dummy, F
        DECF Byte_Count, F
        BTFSC STATUS, Z
        RETURN
        MOVFW Line_Brk
        SUBWF Dummy, W
        BTFSS STATUS, Z ;LCD Line1 full?
        GOTO disp_loop ;no
        CALL Init_Line2
        GOTO disp_loop

;Convert HEX to ASCII for LCD
Make_ASCII MOVWF BCD_Byte
        SWAPF BCD_Byte, W
        ANDLW 0x0F
        IORLW 0x30
        MOVWF Temp_ASC
        SUBLW 0x39 ;check to see if A-F
        BTFSC STATUS, C
        GOTO Mk_ASCII_1
        MOVLW d'7'
        ADDWF Temp_ASC, F
Mk_ASCII_1 MOVFW Temp_ASC
        CALL Write_LCD
        MOVFW BCD_Byte
        ANDLW 0x0F
        IORLW 0x30
        MOVWF Temp_ASC
        SUBLW 0x39 ;check to see if A-F
        BTFSC STATUS, C
        GOTO Mk_ASCII_2
        MOVLW d'7'
        ADDWF Temp_ASC, F
Mk_ASCII_2 MOVFW Temp_ASC
        CALL Write_LCD
        RETURN

;-----------------------------------
; Serial Port Routines
;-----------------------------------

Init_Serial CLRF New_Msg
        CLRF Byte_Count
        BSF TXSTA, BRGH ;high speed mode
        BSF BAUDCTL, BRG16
        MOVLW d'16'
        MOVWF SPBRG ;115k baud at 8-MHz clock
        MOVFW RCREG ;clear interrupt
        BSF TXSTA, TXEN ;enable transmitter
        BSF RCSTA, SPEN ;serial port enable
        BSF RCSTA, CREN ;continuous RX enable
        BSF INTCON, PEIE ;peripheral interrupt enable
        BSF INTCON, GIE ;general interrupt enable
        RETURN

TX_Serial BTFSS PIR1, TXIF ;TX interrupt: 1 = TXREG is empty
        GOTO TX_Serial ;not empty
        MOVWF TXREG ;ok to transmit
        RETURN

Overflow BCF RCSTA, SPEN ;disable serial port
        MOVFW RCREG ;clear interrupt
        BSF RCSTA, SPEN ;enable serial port (reset)
        RETURN

;----------------------------------------
; LCD Routines
;----------------------------------------

Init_LCD CALL Delay100ms ;allow LCD time to reset
        MOVLW Cmnd_Mode ;all init done in LCD command mode
        MOVWF Reg_Select
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay4ms ;Delay greater than 4.1ms
        CALL Delay100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x03 ;LCD sees 30 hex
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x02 ;Set 4-bit mode (LCD sees 20 hex)
        CALL Cmd_8_Bit
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x28 ;Set for 4-bit mode, 16 chars, 2 lines
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x01 ;clear display
        CALL Write_LCD
        CALL Delay4ms ;Delay greater than 4ms
        MOVLW 0x06 ;Entry mode, increment DDRAM, no shift
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW 0x0C ;Display on, cursor off
        CALL Write_LCD
        CALL Delay100us ;Delay greater than 100us
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Cmd_8_Bit MOVWF LCD_PORT ;byte to write will be in W
        BCF Select ;set for command mode
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        RETURN

Write_LCD MOVWF LCD_Data ;byte to write will be in W
        SWAPF LCD_Data, W ;send upper nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF LCD_PORT
        BSF Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF Select ;set for command mode instead
        CALL Delay50us
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        MOVFW LCD_Data ;send lower nibble
        ANDLW 0x0F ;clear upper 4 bits of W
        MOVWF LCD_PORT
        BSF Select ;preset for data mode
        BTFSS Reg_Select, 0 ;0 = command mode, 1 = data mode
        BCF Select ;set for command mode instead
        BSF Enable ;write data to LCD
        NOP
        BCF Enable
        RETURN

Init_Line2 MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVLW 0xC0 ;write at start of line 2 (address 0x40)
        CALL Write_LCD
        CALL Delay100us
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Clear_LCD MOVLW Cmnd_Mode
        MOVWF Reg_Select
        MOVLW 0x01 ;clear display
        CALL Write_LCD
        CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        MOVLW Data_Mode
        MOVWF Reg_Select
        RETURN

Scan_Msg CALL Clear_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW 'Y'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Bad_Scan CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'S'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
Tilt BSF WDTCON, SWDTEN ;force watchdog timeout
tilt1 GOTO tilt1

Bad_Write CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'W'
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        GOTO Tilt

Bad_Read CALL Clear_LCD
        MOVLW 'B'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        GOTO Tilt

Auth_Msg CALL Clear_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'H'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'N'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'C'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        CALL Delay1sec
        RETURN

Done_Msg CALL Clear_LCD
        MOVLW 'R'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW 'M'
        CALL Write_LCD
        MOVLW 'O'
        CALL Write_LCD
        MOVLW 'V'
        CALL Write_LCD
        MOVLW 'E'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVLW 'T'
        CALL Write_LCD
        MOVLW 'A'
        CALL Write_LCD
        MOVLW 'G'
        CALL Write_LCD
        CALL Delay1sec
        CALL Delay1sec
        RETURN

Disp_UID CALL Clear_LCD
        MOVLW 'U'
        CALL Write_LCD
        MOVLW 'I'
        CALL Write_LCD
        MOVLW 'D'
        CALL Write_LCD
        MOVLW ':'
        CALL Write_LCD
        MOVLW ' '
        CALL Write_LCD
        MOVFW UID1
        CALL Make_ASCII
        MOVFW UID2
        CALL Make_ASCII
        MOVFW UID3
        CALL Make_ASCII
        MOVFW UID4
        CALL Make_ASCII
        CALL Delay1sec
        CALL Delay1sec
        RETURN

;-----------------------------------
; Delay routines (8-MHz clock)
;-----------------------------------

Delay50us MOVLW d'24'
        GOTO Cntdwn

Delay100us MOVLW d'48'
        GOTO Cntdwn

Delay1ms MOVLW d'249'
        CALL Cntdwn
        MOVLW d'249'
        GOTO Cntdwn

Delay4ms CALL Delay1ms
        CALL Delay1ms
        CALL Delay1ms
        GOTO Delay1ms

Delay100ms MOVLW d'100'
        MOVWF Delay_Cnt
loop100ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop100ms
        RETURN

Delay250ms MOVLW d'250'
        MOVWF Delay_Cnt
loop250ms CALL Delay1ms
        DECFSZ Delay_Cnt, F
        GOTO loop250ms
        RETURN

Delay1sec CALL Delay250ms
        CALL Delay250ms
        CALL Delay250ms
        CALL Delay250ms
        RETURN

Cntdwn ADDLW -1 ;decrement W
        BTFSS STATUS, Z ;Zero flag set?
        GOTO Cntdwn ;No, keep looping
        RETURN ;Yes, timeout done
;-------------------------------------------------------------------------------

        END